## Slide 1: intro2PCBdesign – lab64
bad boards

## Slide 2: board1

## Slide 3: board1
Trace loops
  EMI disaster

## Slide 4: board1
Trace loops
  EMI disaster
  Loops of wires creates an antenna; aka “Loop antenna”

## Slide 5: board1
Trace loops
  EMI disaster
  Loops of wires creates an antenna; aka “Loop antenna”
Acute trace angles
  Induced coupling between traces

## Slide 6: board1
Trace loops
  EMI disaster
  Loops of wires creates an antenna; aka “Loop antenna”
Acute trace angles
  Induced coupling between traces
    Induces noise in those traces

## Slide 7: board1
Trace loops
  EMI disaster
  Loops of wires creates an antenna; aka “Loop antenna”
Acute trace angles
  Induced coupling between traces
    Induces noise in those traces
These faults will destroy any high frequency projects.

## Slide 8: board2

## Slide 9: board2
Different widths on the same trace

## Slide 10: board2
Different widths on the same trace
  Different impedances on same trace

## Slide 11: board2
Different widths on the same trace
  Different impedances on same trace
    Reflections in high frequency signals
      Byebye signal

## Slide 12: board2
Different widths on the same trace
  Different impedances on same trace
    Reflections in high frequency signals
      Byebye signal
Acute angles

## Slide 13: board3

## Slide 14: board3
Different signal, but parallel traces

## Slide 15: board3
Different signal, but parallel traces
  Induces coupling
    Induces noise
Adjacent signal layers

## Slide 16: board3
Different signal, but parallel traces
  Induces coupling
    Induces noise
Adjacent signal layers
  No ground plane in between can induce noise
    Ground bounce (where is ground?)

## Slide 17: board3
Different signal, but parallel traces
  Induces coupling
    Induces noise
Adjacent signal layers
  No ground plane in between can induce noise
    Ground bounce (where is ground?)
Bad component placement makes bad trace routing seem like a good idea

## Slide 18: board4

## Slide 19: board4
Mismatched lengths for a critical signal

## Slide 20: board4
Mismatched lengths for a critical signal
  Different lengths means different arrival times

## Slide 21: board4
Mismatched lengths for a critical signal
  Different lengths means different arrival times
Outer trace = 1.6105 in
Inner trace = 1.2625 in
Difference = 0.348 in
Dielectric Constant FR-4 dielectric ~= 4
Speed of EM signal in a vacuum ~= 11.8in/ns
Very rough estimate:
  Td = 0.348 in / (11.8 in/ns / sqrt(Ereff)) =50ps delay in propagation
https://blog.zuken.com/how-to-calculate-trace-length-from-time-delay-value-for-high-speed-signals/

## Slide 22: board4
Mismatched lengths for a critical signal
  Different lengths means different arrival times
Outer trace = 1.6105 in
Inner trace = 1.2625 in
Difference = 0.348 in
Dielectric Constant FR-4 dielectric ~= 4
Speed of EM signal in a vacuum ~= 11.8in/ns
Very rough estimate:
  Td = 0.348 in / (11.8 in/ns / sqrt(Ereff)) =50ps delay in propagation
  Rise times for modern digital signals are faster than this!
https://blog.zuken.com/how-to-calculate-trace-length-from-time-delay-value-for-high-speed-signals/